Introduction

This paper introduces a unique design of a pseudo-random sequence generator (PRSG). It conceptually differs from a typical register based PRSG because it exploits some properties of the specific sequence generator and attempts to minimize the number of times data must be written in an attempt to reduce power. While this approach may not have been especially successful because necessary overhead circuitry is only amortized over 5 bits of data, it is still academically interesting, or possibly useful in larger PRSGs.

Pseudo Random Bit Generator Design

Top Level Design

The original top level design of circuit for this project was significantly altered to reduce power consumption. These improvements come from several properties of the specific PRSG given for the assignment.
First, because the first and third registers in the original schematic are used to produce the output, the chain of registers can be split into an 'odd' path and an 'even' path and clocking each of these paths on alternating rising edges of the global clock. The output is produced by multiplexing the output of the even and odd paths. Because the registers do not change on every rising edge of the clock, the output of each XOR gate has an entire clock cycle to propagate to the multiplexer before it is needed. To implement this design, 3 registers are needed on each path, giving a total of 6 registers. This design is beneficial because it reduces the effective clock rate of the registers by half and allows the bit to be output an additional clock cycle to propagate.
Second, by using a latch based design, the total number of latches used in the circuit can be reduced by 1/3. To achieve this reduction, a 4-phase non-overlapping clock must be produced, where the phase changes on both the rising and falling edges of the global clock. To demonstrate this reduction, consider the case of storing 3 bits. A register based design would need 3 registers (and therefore 6 latches) to hold all the data. A latch based design can store the data in 4 latches, where each latch is connected to a different phase of a 4-phase clock. In this case, one latch is accepting data at any given time, and each of the other 3 are holding data. So, 6 latches in a register based design perform the same functionality as 4 latches in a purely latch based design.
The top level design presented in #### was created by using a latch based design with even and odd paths. The total design requires 7 latches. Four latches can store 3 bits, and both the even and odd chains must store 3 bits. This would result in 8 latches; however, the last latch in each chain can be shared between both chains. This design requires a 4-phase non-overlapping clock. In the following discussion of the design, the latches in the odd chain shall be called Q1, Q3, and Q5, and the latches in the odd chain shall be called Q2, Q4, and Q6. The shared latch will be called Q7. Q1 through Q4 roughly correspond to the registers in the original design, so the XOR of Q1-Q3 and Q2-Q4 will be one of the bits in the pseudo-random sequence. The sequence of events for the circuit is summarized in Table 1, below. At any given time, two latches do not contain valid data, so a total of 5 bits are valid at any given time (as should be expected when compared to a register based design). Two sequences of data writes are occuring with one clock cycle delay between the two: {1, 3, 5, 7} and {2, 4, 6, 7}. In this design, the output of an XOR gate does not have a full extra clock cycle to propagate, because one of the latches is being written at the falling edge of the clock, however, an extra half clock cycle is still available. Because of this, the circuit's delay is limited almost entirely by the delay of the 4-phase clock generator.

Clock Phase/Global Clock State	Output	Latches being written
1/High	Q1 XOR Q3	2, 5
2/Low	Q1 XOR Q3	4, 7
3/High	Q2 XOR Q4	6, 1
4/Low	Q2 XOR Q4	7, 3

Table 1: Sequence of Events

The latches selected for this design were dynamic not-D latches. By making the latches inverting, a static inverter is saved between each stage. Dynamic latches were chosen because they require much less power to switch and the data needs to be stored only briefly. The schematic can be seen in ####. The inversion between Q1-Q3 and Q2-Q4 requires a slight modification of the output circuitry.

Output Circuitry

The output circuitry can be seen in the top level view of the schematic (####). It is significantly altered from the original design in the project assignment. First, as the data in Q1 will be the inverted from the value that it read from Q3, the XOR gate in the project assignment must be converted to an XNOR gate. This is a very superficial change because an XOR gate internally inverts one of the signals. Swapping the inverted and original signal results in an XNOR gate. Also, because the latches used in this design are not static, Q1-Q4 require static inverters to drive the XNOR gate. Lastly, a transmission gate multiplexer and additional buffering were added. One of the inverters in the buffer occurs before the multiplexer to reduce propagation delay after the inverter switches.
The ordering of the connections to the input terminals of the XNOR gate, as seen in ####, are also important. Because one input terminal has an additional inverter to propagate through, that terminal has additional propagation delay. Q1 and Q2 were connected to this terminal, because they are stable before Q3 and Q4.

Sequencer Circuit

The sequencer circuit produces the 4-phase non-overlapping clock signals and the signals that control the output multiplexer. It can be seen in ####. The three sections of the circuit are: differential clock generator, 4-phase clock generator, and divided clock generator (divide by 2).
The five inverters produce a differential clock signal. The sizes of the cross coupled inverters control the amount of clock skew in the circuit's output. The larger they are in comparison to the other inverters, the lower the clock skew. This section of the circuit was sized to drive only the 4-phase clock generator.
The 4-phase clock generator is very similar to a typical 2-phase non-overlapping clock generator. Because the circuit is implemented with NAND gates, the clock phases pulse low. Each phase cannot fall until both of the two previous stages have risen, and the clock signal is used to synchronize the phases to the differential clock. The sequencer circuit also generates the complement of the 4-phase clock signals using inverters two inverters in series. The first of this pair helps the signal to be non-overlapping; it has a PMOS to NMOS width ratio is one, which causes each phase to turn off faster than it turned on. The odd sizing of this inverter was crucial to making this design work.
The NAND3 gate used for the 4 phase clock generator, as seen in ####, is slightly unusual; the only PMOS needed is the one attached to the differential clock. The other two PMOS can be removed because they are disabled on the rising edge of the output waveform. These 2 PMOS would account for a substantial portion of the total capacitance of the 4-phase clock generator if they were not removed.
The divided clock generator (so named because it switches once per cycle) produces the signals that control the output multiplexers at the top level. It can be seen in #### (the pair of charge pumps). It was originally implemented as 2 NAND2 gates, where each gate produces either the divided clock or its complement. However, because each phase is mutually exclusive, each NAND gate simplifies to a charge pump.

Reset Circuit

When desigining the reset circuitry, the goal was to use the clock signal as little as possible to minimize power consumption. Because the reset is assumed to switch very seldom, it does not contribute signifcantly to total power usage. Additionally, the internal reset signal for this design must be high for only the first half of the clock cycle because data is being written on both the rising and falling edges of the clock.
The final design for the reset circuitry, as seen in ####, meets both these specifications. It consists of a rising edge detector, an SR-latch, a not-D latch, a NAND gate, and drive/delay circuitry. The SR-latch is set on the rising edge of the reset signal. The not-D register and NAND gate delay the internal reset signal until the next clock rising edge. The internal reset signal pulls each latch (that hold the pseudo-random sequence) either high or low and resets the SR-latch. The only load presented to the clock is the not-D latch and the NAND gate. The circuit will not switch at all unless a rising edge has been detected on the external reset signal.
The SR-latch is implemented as a static latch because the circuit might not be reset for a long time, whereas the not-D latch is dynamic because a rising edge must be checked for on every clock cycle.

Layout of the Design

To minimize the footprint of the pseudo random bit sequence generator, layout was designed as shown in the Figure ##. Each block is rotated and placed in a way to make the design more compact, minimize the wasted space and short wiring. Similar color in the figure represents similar functionality. For example, green was used for sequencer circuit which is composed of differential clock generator, four-phase clock generator, and divided clock generator.
Dynamic latches (1~6) are the core of PRSG and have the most connections with peripheral circuitries; hence it was placed in the center. The numbers corresponds to the latches described in the schematic. Latch 7 is a temporary storage of the output feedback. Latch 5 and 6 are the first stages which are connected from latch 7 and other latches are place in order towards the output. For the correct behavior of each latch when reset signal is high, pull up/pull down transistors were attached on the sides for quick response. Since dynamic latch with four transistors were implemented, every other stage will have the same output value but neighboring latches will result in the inverted values. In result, pull up and pull down transistors were altered. Reset circuitry was placed at the right end of the layout since it takes quite a large area and it will be more convenient to connect to reset transistors.
Clock generators were placed at the bottom to have efficient connection to all the latches in the center. Control signals for the dynamic latches are from four-phase clock generator; therefore it was placed right below the latch chains. Differential clock generator is placed near reset and four-phase clock generator because it mainly sends both synchronous clock and clock bar signal to both circuits. Divided clock generator is only connected to the transmission gates of the output circuitry hence why it was placed on the left side of the clock generator where the transmission gates are located in the output circuitry.
Output circuitry is place on the remaining side which is placed next to (or above) the latches that are connected to the input of the output circuitry. Two identical output circuits were inserted to handle each output of two parallel latch chains. However, it was combined with a single output buffer (large inverter) since only one of the circuits will be transferring the data. Another purple block is found under the output circuitry which is an inverter that buffers the signal from the output circuitry.
The overall area of the layout is 886.982um2 (Length=28.32um, Width=31.32um). Latch chains were small compare to registers with less number of transistors, but other circuitry took decent amount of space in the layout. However, if the number of bits from the pseudo random bit sequence generator is increased, we will have to implement more latches (or registers in other designs), then we will benefit in area and power consumption from this design.

Figure 1. Complete PRSG (Toplevel) Layout Block Diagram

Simulation Results

Power Consumption

The power spent on latches in this design is dramatically lower than in a register based design. The original design requires 20 latches to be written in two clock cycles, whereas this design only requires 8 latches to be written. However, this design has a reasonable amount of overhead associated with producing the 4-phase clock, and multiplexing the outputs.

Group Contributions

There were several modifications and challenges during the process of design. Several candidate schematics and layouts were drawn and simulated which turned out to have few problems.

Robert Mertens
I redesigned the top level design of the schematic, and helped with some of the layout. I also wrote the part of this report discussing the conceptual design of this project. I mostly worked on latch design and the timing circuitry.
Wenxun Huang

Nikhil Ramans
Could not be reached for comment.
Leslie Hwang
I worked on the schematic and hspice simulation of several early designs and layout drawing and optimization. Sizing the transistors of the output circuitry to drive the load capacitance was also done from the hspice simulation and some calculation. For the project report, I have worked on the layout description.